## Slide 1: EECS 370 Discussion
Calvin and Hobbes
by Bill Watterson

## Slide 2: EECS 370 Discussion
Exam
7:00 – 8:30 Tuesday (Tomorrow!)
Bring:
    Pencil
    Calculator
    Notes Sheet
      letter-sized, double sided, 1 sheet

## Slide 3: EECS 370 Discussion
Exam Review
Multi-cycle Datapath
Pipeline Datapath
  Hazards!
Caches

## Slide 4: EECS 370 Discussion
Multi-Cycle Datapath

## Slide 5: EECS 370 Discussion
Multi-Cycle Datapath

## Slide 6: EECS 370 Discussion
Multi-Cycle Datapath
Frequency as compared to single-cycle?
Do all instructions take the same amount of time?
What is the CPI for a multi-cycle machine?

## Slide 7: EECS 370 Discussion
Multi-Cycle Datapath
Frequency as compared to single-cycle?
Higher
Do all instructions take the same amount of time?
No! (ADD, NAND, SW, BEQ: 4 cycles, LW: 5 cycles)
What is the CPI for a multi-cycle machine?
Depends on the instructions you run through it

## Slide 8: EECS 370 Discussion
Multi-Cycle Datapath
Why doesn’t multi-cycle have data hazards or control hazards?
What does the red Control circle on the diagram do?

## Slide 9: EECS 370 Discussion
Multi-Cycle Datapath
Why doesn’t multi-cycle have data hazards or control hazards?
Only one instruction is running at a time
What does the red Control circle on the diagram do?
Sets the control signals for
muxes, ALU, Memory, and Reg

## Slide 10: EECS 370 Discussion
Multi-Cycle Datapath
Let’s run an instruction through the datapath

## Slide 11: EECS 370 Discussion
Pipeline Datapath

## Slide 12: EECS 370 Discussion
Pipeline Datapath
Frequency as compared to single-cycle?
Do all instructions take the same amount of time?
What is the CPI for a pipelined processor?

## Slide 13: EECS 370 Discussion
Pipeline Datapath
Frequency as compared to single-cycle?
Higher
Do all instructions take the same amount of time?
Yes
What is the CPI for a pipelined processor?
1 (over many instructions)

## Slide 14: EECS 370 Discussion
Pipeline Datapath
Timing Example
1000 Instructions:
What is the total execution time? (No Hazards)
25% lw
5% sw
50% add/nand
20% beq
6 ns – Register Read/Write
2 ns – ALU Operations
10 ns – Memory Access

## Slide 15: EECS 370 Discussion
Pipeline Datapath
Timing Example
1000 Instructions:
What is the total execution time? (No Hazards)
10 * (4+1000) = 10040 ns
25% lw
5% sw
50% add/nand
20% beq
6 ns – Register Read/Write
2 ns – ALU Operations
10 ns – Memory Access

## Slide 16: EECS 370 Discussion
Data Hazards
Avoidance
Detect and Stall
Detect and Forward

## Slide 17: EECS 370 Discussion
Pipeline Datapath
Timing Example
1000 Instructions:
37% of ADD/NAND instructions followed by dependent instruction
Detect and forward
What is the total execution time?
25% lw
5% sw
50% add/nand
20% beq
6 ns – Register Read/Write
2 ns – ALU Operations
10 ns – Memory Access

## Slide 18: EECS 370 Discussion
Pipeline Datapath
Timing Example
1000 Instructions:
37% of ADD/NAND instructions followed by dependent instruction
Detect and forward
What is the total execution time?
10 * (4+1000) = 10040 ns
25% lw
5% sw
50% add/nand
20% beq
6 ns – Register Read/Write
2 ns – ALU Operations
10 ns – Memory Access

## Slide 19: EECS 370 Discussion
Control Hazards
No Branches
Avoid
Detect-and-stall
Speculate-and-squash

## Slide 20: EECS 370 Discussion
Control Hazards
In a 27 stage pipeline, if Branches are resolved in Stage 14:
Which stages must be squashed?

## Slide 21: EECS 370 Discussion
Control Hazards
In a 27 stage pipeline, if Branches are resolved in Stage 14:
Which stages must be squashed?
Stages 1 through 13

## Slide 22: EECS 370 Discussion
Pipeline Datapath
Timing Example
1000 Instructions:
10% of BEQ instructions are mispredicted
Speculate-and-squash
What is the total execution time?
25% lw
5% sw
50% add/nand
20% beq
6 ns – Register Read/Write
2 ns – ALU Operations
10 ns – Memory Access

## Slide 23: EECS 370 Discussion
Pipeline Datapath
Timing Example
1000 Instructions:
10% of BEQ instructions are mispredicted
Speculate-and-squash
What is the total execution time?
10 * (4+1000 + 1000*0.2*0.1*3) = 10640 ns
25% lw
5% sw
50% add/nand
20% beq
6 ns – Register Read/Write
2 ns – ALU Operations
10 ns – Memory Access

## Slide 24: EECS 370 Discussion
Branch Predictors
Pattern is:
N N N T (Starting at Strongly Taken)
What is the mispredict rate?
Weakly Taken
Strongly Taken
Taken
Not Taken
Strongly
Not Taken
Weakly Not Taken
Taken
Not Taken
Taken
Not Taken

## Slide 25: EECS 370 Discussion
Branch Predictors
Pattern is:
N N N T (Starting at Strongly Taken)
What is the mispredict rate? 25%
Weakly Taken
Strongly Taken
Taken
Not Taken
Strongly
Not Taken
Weakly Not Taken
Taken
Not Taken
Taken
Not Taken

## Slide 26: EECS 370 Discussion
Caches
What are the types of Locality?
What’s the calculation for Block Index bits?
What’s the calculation for Set Index bits?

## Slide 27: EECS 370 Discussion
Caches
What are the types of Locality?
Spatial & Temporal
What’s the calculation for Block Index bits?
log2(block size)
What’s the calculation for Set Index bits?
log2(number of sets)

## Slide 28: EECS 370 Discussion
Types of Caches
Fully Associative
Blocks map to any cache line
Cache | 
Tag | Data
Memory | 
0x1000 | 10
0x1004 | 20
0x1008 | 30
0x100C | 40
0x1010 | 50
0x1014 | 60
0x1018 | 70
0x101C | 80
0x1020 | 90
0x1024 | 100
0x1028 | 110

## Slide 29: EECS 370 Discussion
Types of Caches
Direct Mapped
Blocks map to one cache line
Cache | 
Tag | Data
Memory | 
0x1000 | 10
0x1004 | 20
0x1008 | 30
0x100C | 40
0x1010 | 50
0x1014 | 60
0x1018 | 70
0x101C | 80
0x1020 | 90
0x1024 | 100
0x1028 | 110

## Slide 30: EECS 370 Discussion
Types of Caches
Set Associative
Blocks map to any line in a set
Cache | 
Tag | Data
Memory | 
0x1000 | 10
0x1004 | 20
0x1008 | 30
0x100C | 40
0x1010 | 50
0x1014 | 60
0x1018 | 70
0x101C | 80
0x1020 | 90
0x1024 | 100
0x1028 | 110

## Slide 31: EECS 370 Discussion
Caches
What are the Three C’s and how do we determine them?

## Slide 32: EECS 370 Discussion
Caches
What are the Three C’s and how do we determine them?
Compulsory – if we have never loaded it
Capacity – misses in same size fully associative cache
Conflict – any additional misses in actual cache

## Slide 33: EECS 370 Discussion
Caches
What’s the difference between Write Allocate and
No Write Allocate?
What’s the difference between Write Through and Write Back?

## Slide 34: EECS 370 Discussion
Caches
What’s the difference between Write Allocate and
No Write Allocate?
Write Allocate – add to cache on write miss
No Write Allocate – don’t add to cache
What’s the difference between Write Through and Write Back?
Write Through – always write to memory
Write Back – just write to cache

## Slide 35: EECS 370 Discussion
Caches
Timing Example
1000 Instructions:
10% of BEQ instructions are mispredicted, Speculate-and-squash
20% of all memory accesses miss caches. Misses take 20 cycles
What is the total execution time?
25% lw
5% sw
50% add/nand
20% beq
6 ns – Register Read/Write
2 ns – ALU Operations
10 ns – Memory Access

## Slide 36: EECS 370 Discussion
Caches
Timing Example
1000 Instructions:
10% of BEQ instructions are mispredicted, Speculate-and-squash
20% of all memory accesses miss caches. Misses take 20 cycles
What is the total execution time?
10 * (4+1000 + 1000*0.2*0.1*3)
+ 10 * (1000*.2*20 + 1000*.25*.2*20 +1000*.05*.2*20) = 62640 ns
25% lw
5% sw
50% add/nand
20% beq
6 ns – Register Read/Write
2 ns – ALU Operations
10 ns – Memory Access