## Slide 1: EECS 370 Discussion
xkcd.com

## Slide 2: EECS 370 Discussion
Topics Today:
  Floating Point
  Finite State Machines
  Combinational Logic
  Sequential Logic

## Slide 3: EECS 370 Discussion
Floating Point
Exponent
Biased by 127
Significand
Additional 1 before the decimal sign

## Slide 4: EECS 370 Discussion
Floating Point
Don’t forget about zero!

## Slide 5: EECS 370 Discussion
Floating Point
Addition
-1.1011*(22) + 1.01*(20)

## Slide 6: EECS 370 Discussion
Floating Point
Addition
-1.1011*(22) + 1.01*(20)
= -1.0110*(22)

## Slide 7: EECS 370 Discussion
Floating Point
Addition
-1.1011*(22) + 1.01*(20)
[-6.75] [1.25]
= -1.0110*(22)
[-5.5]

## Slide 8: EECS 370 Discussion
Floating Point
Multiplication
-1.1011*(22) * 1.01*(20)
[-6.75] [1.25]

## Slide 9: EECS 370 Discussion
Floating Point
Multiplication
-1.1011*(22) * 1.01*(20)
[-6.75] [1.25]
= -1.0000111*(23)

## Slide 10: EECS 370 Discussion
Floating Point
Multiplication
-1.1011*(22) * 1.01*(20)
[-6.75] [1.25]
= -1.0000111*(23)
[-8.4375]

## Slide 11: EECS 370 Discussion
Finite State Machines
Diagram of State, Conditions to change state, and Outputs
Conditions to change are based on inputs

## Slide 12: EECS 370 Discussion
Finite State Machines
Example: Output a 1 on the pattern 001
States:
Pattern ‘1’
Pattern ‘0’
Pattern ‘00’
Pattern ‘001’ => Output = 1

## Slide 13: EECS 370 Discussion
Combinational Logic
Digital circuit representing a Boolean equation
Truth tables!!

## Slide 14: EECS 370 Discussion
Combinational Logic
More Complex Circuits:
Mux Decoder
A
S
B
C
Out1
Out2
A0
A1
Out3
Out0

## Slide 15: EECS 370 Discussion
Combinational Logic
More Complex Circuits: Full Adder
Half Adder

## Slide 16: EECS 370 Discussion
Combinational Logic
More Complex Circuits:
Ripple Carry Adder

## Slide 17: EECS 370 Discussion
Combinational Logic
Propagation Delay

## Slide 18: EECS 370 Discussion
Combinational Logic
Propagation Delay
Slows down the speed of your circuit!

## Slide 19: EECS 370 Discussion
Combinational Logic
Most Complex Circuits:
Carry Look-ahead Adder

## Slide 20: EECS 370 Discussion
Sequential Logic
Combinational Logic
Stateless
Output is direct function of current input
Sequential Logic
Stateful
Output is function of current input and past input
Clocked!

## Slide 21: EECS 370 Discussion
Sequential Logic
Latches
SR Latch D Latch

## Slide 22: EECS 370 Discussion
Sequential Logic
Flip Flops
Positive Edge Triggered

## Slide 23: EECS 370 Discussion
Sequential Logic
Why do we want clocked logic?
Specifies a time by which all operations are “done”
Results before that time do not matter

## Slide 24: An Example of why this matters
Delays in combinational circuits are very real.
Here’s an example with a ripple carry adder.

## Slide 25: An Example of why this matters
Let’s zoom in on the interesting part.
The value of a goes from 7 to 1 here

## Slide 26: An Example of why this matters
Let’s zoom in on the interesting part.
There’s propagation delay before the adder even starts to change values.

## Slide 27: An Example of why this matters
Let’s zoom in on the interesting part.
The value stabilizes

## Slide 28: An Example of why this matters
Let’s zoom in on the interesting part.
The next clock edge comes along

## Slide 29: An Example of why this matters
Let’s zoom in on the interesting part.
The latch opens up
(and shows new value)
The flip-flop grabs new value.

## Slide 30: An Example of why this matters
Let’s zoom in on the interesting part.
B changes now,
while the clock is still high.

## Slide 31: An Example of why this matters
Let’s zoom in on the interesting part.
Again, there’s propagation delay before the adder starts to change.

## Slide 32: An Example of why this matters
Let’s zoom in on the interesting part.
The value in the latch changes too!

## Slide 33: An Example of why this matters
Let’s zoom in on the interesting part.
The next falling edge comes along

## Slide 34: An Example of why this matters
Let’s zoom in on the interesting part.
The adder stabilizes.

## Slide 35: An Example of why this matters
Let’s zoom in on the interesting part.
The latch locked with the wrong value!