## Slide 1: EECS 370 Discussion
smbc-comics.com

## Slide 2: EECS 370 Discussion
Topics Today:
  5-stage Pipeline
    Basic Design
    Performance
    Data Hazards
  Exams

## Slide 3: EECS 370 Discussion
Single Cycle
CPI =
Clock Period =

## Slide 4: EECS 370 Discussion
Single Cycle
CPI = 1
Clock Period = long
Multi-Cycle
CPI =
Clock Period =

## Slide 5: EECS 370 Discussion
Single Cycle
CPI = 1
Clock Period = long
Multi-Cycle
CPI = >1
Clock Period = short
Pipelined
CPI =
Clock Period =

## Slide 6: EECS 370 Discussion
Single Cycle
CPI = 1
Clock Period = long
Multi-Cycle
CPI = >1
Clock Period = short
Pipelined
CPI ≈ 1
Clock Period = short

## Slide 7: EECS 370 Discussion
5-stage Pipeline

## Slide 8: EECS 370 Discussion
5-stage Pipeline
Pipeline Example
    add 1 2 3
    nand 4 5 6
    lw 0 4 26
    add 2 2 2
    nand 1 1 1

## Slide 9: EECS 370 Discussion
5-stage Pipeline
Key Concept
1000 instructions are run on a 5-stage pipeline (no hazards)
How many cycles are needed to complete them?

## Slide 10: EECS 370 Discussion
5-stage Pipeline
Key Concept
1000 instructions are run on a 5-stage pipeline (no hazards)
How many cycles are needed to complete them?
1004 cycles

## Slide 11: EECS 370 Discussion
Multi-Cycle Datapath
Timing Example
100 Instructions:
What is the total execution time? (No Hazards)
Single Cycle: 100 * 60 = 6000 ns
Multi-Cycle: 20 * (35*5 + 15*4 + 30*4 + 20*4) = 8700 ns
Pipelined:
35% lw
15% sw
30% add/nand
20% beq
5 ns – Register Read/Write
10 ns – ALU Operations
20 ns – Memory Access

## Slide 12: EECS 370 Discussion
Multi-Cycle Datapath
Timing Example
100 Instructions:
What is the total execution time? (No Hazards)
Single Cycle: 100 * 60 = 6000 ns
Multi-Cycle: 20 * (35*5 + 15*4 + 30*4 + 20*4) = 8700 ns
Pipelined: 20 * (4 + 100) = 2080 ns
35% lw
15% sw
30% add/nand
20% beq
5 ns – Register Read/Write
10 ns – ALU Operations
20 ns – Memory Access

## Slide 13: EECS 370 Discussion
Data Hazards
Key Concepts
In what stage is data read from registers?
In what stage is data written to registers?

## Slide 14: EECS 370 Discussion
Data Hazards
Key Concepts
In what stage is data read from registers?
Decode
In what stage is data written to registers?
Writeback

## Slide 15: EECS 370 Discussion
Data Hazards
The Problem:
x = 5*y+3;
LDR R1 [R0, #wherever y is]
MUL R2 R1 #5
ADD R2 R2 #3
STR R2 [R0, #wherever x is]

## Slide 16: EECS 370 Discussion
Data Hazards
Solutions:
Avoidance
Detect and Stall
Detect and Forward

## Slide 17: EECS 370 Discussion
Data Hazards
Pipeline Example
    add 1 2 3
    nand 3 5 6
    lw 0 3 26
    add 6 2 4
    nand 4 3 1

## Slide 18: EECS 370 Discussion
Exam Results
Answer Keys are posted online
Exams will be returned now next week
Regrade Requests:
  Submit Scantron + written statement to IA/GSI/Professor
  Before Friday