## Slide 1: EECS 370 Discussion
xkcd.com

## Slide 2: EECS 370 Discussion
Topics Today:
  Control Hazards
  Branch Prediction
  Project 3
  stackoverflow Example

## Slide 3: EECS 370 Discussion
Control Hazards
Key Concept
Which LC-2K instruction(s) can cause a Control Hazard?
In which stage are branches resolved?

## Slide 4: EECS 370 Discussion
Control Hazards
Key Concept
Which LC-2K instruction(s) can cause a Control Hazard?
BEQ & JALR
In which stage are branches resolved?
MEM

## Slide 5: EECS 370 Discussion
Control Hazards
Problem:
If we don’t know what the next PC should be
what do we do?
Options:
No Branches
Avoid
Detect-and-stall
Speculate-and-squash

## Slide 6: EECS 370 Discussion
Control Hazards
No Branches
Is this a feasible solution?
How could we eliminate this if statement?
    if (r0 == r1) {
    r2 = r3;
    } else {
    r2++;
    }

## Slide 7: EECS 370 Discussion
Control Hazards
No Branches
Is this a feasible solution?
How could we eliminate this if statement?
    Conditional Assembly!
    if (r0 == r1) {
    r2 = r3;
    } else {
    r2++;
    }
cmp r0, r1
moveq r2, r3
addne r2, r2, #1

## Slide 8: EECS 370 Discussion
Control Hazards
Avoid
ADD 1 1 1
NAND 2 2 2
BEQ 3 0 jump
ADD 4 4 4
NAND 5 5 5
jump ADD 6 6 6
NAND 7 7 7

## Slide 9: EECS 370 Discussion
Control Hazards
Detect-and-stall
Any better than avoid?

## Slide 10: EECS 370 Discussion
Control Hazards
Speculate-and-squash
Guess!
What do you have to do if you’re correct?
What do you have to do if you’re wrong?

## Slide 11: EECS 370 Discussion
Control Hazards
Speculate-and-squash
Guess!
What do you have to do if you’re correct?
Nothing at all
What do you have to do if you’re wrong?
Turn IF, ID, & EX into Noops

## Slide 12: EECS 370 Discussion
Branch Prediction
Based on the PC
What did this branch do last time?
1-bit predictor
Not Taken
Taken
Taken
Not Taken

## Slide 13: EECS 370 Discussion
Branch Prediction
2-bit predictor
Weakly Taken
Strongly Taken
Taken
Not Taken
Strongly
Not Taken
Weakly Not Taken
Taken
Not Taken
Taken
Not Taken

## Slide 14: EECS 370 Discussion
Branch Prediction
What does the PC become if we predict Not Taken?
What does the PC become if we predict Taken?

## Slide 15: EECS 370 Discussion
Branch Prediction
What does the PC become if we predict Not Taken?
PC+1
What does the PC become if we predict Taken?
???

## Slide 16: EECS 370 Discussion
Branch Prediction
Branch Target Buffer
Maps PC values to Addresses
PC | Address
0x1234 | 0x00001000
0x4523 | 0x00004000
0xA342 | 0x00000004
0xFF76 | 0x0000A342

## Slide 17: EECS 370 Discussion
Branch Prediction
Do we branch? Where?
PC | Address
0x1234 | 0x00001000
0x4523 | 0x00004000
0xA342 | 0x00000004
0xFF76 | 0x0000A342
PC | Address
0x1234 | 
0x4523 | 
0xA342 | 
0xFF76 | 
PC

## Slide 18: EECS 370 Discussion
Project 3
Make your own pipelined processor
Need to use code for the file input from Project 1
Write non-hazard code first
Design good test code!!

## Slide 19: EECS 370 Discussion
WBEND Register and Forwarding
WBEND

## Slide 20: EECS 370 Discussion
stackoverflow example
Real-world example. Why this stuff matters.
http://stackoverflow.com/questions/11227809/why-is-processing-a-sorted-array-faster-than-an-unsorted-array

## Slide 21: EECS 370 Discussion

## Slide 22: EECS 370 Discussion
With this line: 6.54 seconds
Without: 13.84 seconds

## Slide 23: EECS 370 Discussion
With this line: 1.93 seconds
Without: 11.54 seconds

## Slide 24: EECS 370 Discussion
Why is this happening? What is causing the time differences?

## Slide 25: EECS 370 Discussion
Branch Prediction!