## Slide 1: Energy Isolation Required for Multi-tenant Energy Harvesting Platforms
Branden Ghena
Joshua Adkins, Bradford Campbell, Branden Ghena, Neal Jackson, Pat Pannuto, & Prabal Dutta
ENSsys’17
November 5, 2017 - Delft, Netherlands

## Slide 2: It’s time to start thinking about energy-harvesting and multi-tenancy together
How do we support multiple unaligned applications while also balancing limited energy availability?
We need to address energy sharing, isolation, and adaptivity

## Slide 3: Motivation: The Signpost Platform
Enabling city-scale sensing applications
  Platform provides base services
  Modules run applications and include sensors
Infrastructure-free infrastructure
  Solar energy harvesting
  Multiple wireless networking options
  Easy (two bolt) installation

## Slide 4: Signpost expects a variety of applications
Environmental Sensing
RF Spectrum Use Measurement
Motion Detection
Audio Analysis

## Slide 5: Signpost expects energy variability
Daily average varies between 2.7 W and 0.09 W

## Slide 6: Design requirements for Signpost
Energy on Signpost is shared between applications
  Needs individual module energy use measurements
  Needs individual module power control
  Needs to measure and charge for service usage
  Needs to allocate incoming energy among applications
Platform needs to enable adaptable applications
  Expects to be deployed with varying energy availability
  Applications can’t be re-written for each Signpost

## Slide 7: Multiprogramming is coming to single-microcontroller systems too
Systems like Tock and Amulet provide multi-tenancy on low-power, resource-constrained systems
These systems bring new challenges
  Applications may be even further decoupled from the hardware
  Fine-grained measurements of energy use may be difficult
  The platform needs to account for and be able to reset external state

## Slide 8: How do we enable application reasoning?
Guarantee: allocated energy may only decrease predictably
  The application may run and use the energy
  Services may be used that charge against the application
  The platform may charge a constant upkeep cost
Allow applications to plan for the worst-case future

## Slide 9: How should energy be allocated to applications?
Simple: Divide evenly between virtual allocations
Complex: Use energy allocation as a form of priority
Design questions
  Need to decide how much energy each application can store
  Need to decide how frequently to apportion incoming energy
    Lack of care leads to intermittent operation

## Slide 10: Discussion
How do we make energy-limited programming accessible to developers?
Allocation guarantees enable reasoning, but only if applications can access and interpret their energy availability
Do we really want application developers to have to reason about their energy?
Is run-to-completion at a varying frequency the only model that works here?
Notes: Signpost: applications can request a duty cycle, made an API for measurement of ”operation” energy use

## Slide 11: Discussion
How do we enable developers to understand how code is functioning at runtime?
Is compile-time analysis still helpful in a multiprogramming scenario?
How do you report runtime performance of applications?
How do you know in advance that a certain combination of applications is going to have undesirable results?
Notes: Signpost:

## Slide 12: Discussion
When is state-based profiling an accurate enough as a measure of application energy use?
Putting energy gauges everywhere is unlikely for many platforms
Accurately sharing a hardware resource, like a radio, is difficult even with an individual gauge
Notes: Signpost:

## Slide 13: Discussion
What reliability guarantees can we expect from energy-harvesting systems?
How do you distinguish failure from lack of energy?
Can we include energy-harvesting systems in user facing applications?
Notes: Signpost:

## Slide 14: For More Information…
https://github.com/lab11
  lab11/signpost [hardware design files]
  lab11/signpost-software [software repository]
https://github.com/helena-project/tock
Email: brghena@berkeley.edu
Notes: Our lab website is down. Lame 