## Slide 1: Energy-Harvesting Thermoelectric Sensing for Unobtrusive Water and Appliance Metering
Brad Campbell, Branden Ghena, and Prabal Dutta
2nd International Workshop on Energy Neutral Sensing Systems (ENSsys 2014) – November 6, 2014

## Slide 2: The Call for “Low Power Sensors”
“BTO [Building Technologies Office] is particularly interested in innovative approaches that reduce the cost and power consumption for data collection of common building operation variables (temperature, pressure, relative humidity, etc.)…”
Source(s):
“Building Energy Efficiency Frontiers and Incubator Technologies (BENEFIT),” DE-FOA-0001027, 2014
Notes: On Tuesday at SenSys we heard from Thyaga Nandagopal saying that NSF wants energy-harvesting continuous sensors. The Building Technologies Office agrees and calls for new approaches to low power building sensing systems

## Slide 3: An Energy Harvesting Architecture
The Monjolo Family
  Energy-neutral system
  Wireless communications
Light-level
Plug-load
Panel-mount
Notes: This is the Monjolo Principle

## Slide 4: The Monjolo Principle
Monjolo: Portuguese water hammer
In an energy harvesting system:
The rate at which energy is harvested is proportional to the intensity of the measured phenomenon
The energy harvester is the sensor
Notes: This is the Monjolo Principle

## Slide 5: Our System Design
Thermes
  Small form factor
  Thermal energy-harvesting
  Energy-neutral system
  Wireless communication
Notes: We do this by using a new system architecture for water metering devices.

## Slide 6: Thermes System Architecture
Notes: Digging into the architecture that enables Thermes,

## Slide 7: Thermes System Architecture

## Slide 8: Thermes System Architecture

## Slide 9: Thermes System Architecture

## Slide 10: Harvesting Front End
Peltier junctions
  Temperature differential into current
  Low efficiency
Heat rejection is critical
Multiple junctions in series for more voltage
Notes: Curiosity! And Voyager at 37 years…

## Slide 11: Zoom into Power System
Power supply
  Auto-polarity
  Harvesting begins at 30 mV
500 uF capacitor bank
  No battery
Top
Bottom

## Slide 12: Zoom into Latch Circuit
Latch sets size of “bucket” and turns the node core on and off
Turns on at 3.1 V, powers down at 2.1 V
Translates to 1.3 mJ per activation

## Slide 13: Transmission Rate Changes with Temperature
Time
Temperature Differential
Time
Radio Packet
Transmission
Notes: This means that an always-on receiver can receive these radio transmissions and use them to determine the temperature differential

## Slide 14: Zoom into Node Core
The classic node setup
MSP430
  TinyOS
CC2420
  802.15.4 communications
Top
Notes: ~Vintage~

## Slide 15: Our System Design
Thermes
Energy-Neutral Thermal Sensing
But what can you do with such a sensor?
Notes: We do this by using a new system architecture for water metering devices.

## Slide 16: Shower Use Is a Contributing Factor
Consumers don’t have insight into how this energy is being spent
Department of Energy, “Building Energy Data Book.” 2010
American Water Works Association Research Foundation, “Residential End Uses of Water.” 1999

## Slide 17: Existing Water Meters

## Slide 18: Acoustic Water Meters
High powered sensing
  Lifetime limitation
Sprav
Upstream
Notes: These systems are very attractive because they simply clip (or wire) on to a pipe in order to measure water use. Both of these use microphones in order to determine when water is actually running and augment that information with temperature sensors.
The downside here is battery life. The test deployment of Upstream was severely limited by battery life and nodes could only be deployed for 4-7 days without attention.
There are also problems with these devices of limited communications. Sprav attempts to communicate data, but uses Bluetooth to talk to Smartphones. This just doesn’t seem like a great choice to me. I know people take their phones into the bathroom, but into the shower is really one step too far for me…

## Slide 19: Impeller-Based Water Meters
Impeller-based design
  Good for energy harvesting
  Difficult installation
Amphiro

## Slide 20: Thermal Harvesting Water Meters
Thermoelectric energy-harvesting
  Energy-neutral in some cases
Accelerometer-based sensing
  Increases energy needs
DoubleDip

## Slide 21: Applying Our Solution
This is an area for which we designed Thermes
Trade accuracy and fine-grained detail for continuous batteryless operation
Shower sensing is actually very challenging for this system

## Slide 22: Thermes Implementations
Small Bracelet
  6 Peltier Junctions (7 mm x 6 mm)
  9 Heatsinks
Large Bracelet
  4 Peltier Junctions (15 mm x 15 mm)
  4 Heatsinks

## Slide 23: Evaluation Criteria
How does it work at various water temperatures?
How well can it estimate start and stop times?
How well does it work on a real shower?
What other applications can it be used for?

## Slide 24: Evaluation Setup
Mini-shower
Allows for configurable constant water temperature
Ambient temperature remained 23° C for all tests

## Slide 25: Evaluation Setup
Mini-shower
Allows for configurable constant water temperature
Ambient temperature remained 23° C for all tests
Thermes

## Slide 26: Evaluation Criteria
How does it work at various water temperatures?
How well can it estimate start and stop times?
How well does it work on a real shower?
What other applications can it be used for?

## Slide 27: Operation at Average Shower Temperature
Shower On
Shower Off
Small Bracelet
Large Bracelet

## Slide 28: Operation at Average Shower Temperature
Shower On
Shower Off
Small Bracelet
Large Bracelet

## Slide 29: Operation at Average Shower Temperature
Shower On
Shower Off
Small Bracelet
Large Bracelet

## Slide 30: Operation at Average Shower Temperature
Shower On
Shower Off
Small Bracelet
Large Bracelet

## Slide 31: Equilibrium of the System
Time
Temperature of Pipe
Time
Radio Packet
Transmission
Notes: This means that an always-on receiver can receive these radio transmissions

## Slide 32: Equilibrium of the System
Time
Temperature of Pipe
Time
Radio Packet
Transmission
Notes: This means that an always-on receiver can receive these radio transmissions

## Slide 33: Lower Temperature Operation Is Troublesome
Shower On
Shower Off
Small Bracelet
Large Bracelet

## Slide 34: Lower Temperature Operation Is Troublesome
Shower On
Shower Off
Small Bracelet
Large Bracelet

## Slide 35: Evaluation Criteria
How does it work at various water temperatures?
How well can it estimate start and stop times?
How well does it work on a real shower?
What other applications can it be used for?

## Slide 36: Estimating Start and Stop Times
Small Bracelet
Notes: Activation rate changes even though temperature remains the same
This means extra processing is needed to know when the shower started and stopped

## Slide 37: Estimating Start and Stop Times
Determine likely delay before first packet based on initial packet rate
Small Bracelet

## Slide 38: Estimating Start and Stop Times
Look for change in steady state operation
Small Bracelet

## Slide 39: Estimation Example
Test Results
  3 second error on Start Time
  9 second error on Stop Time
Small Bracelet

## Slide 40: Evaluation Criteria
How does it work at various water temperatures?
How well can it estimate start and stop times?
How well does it work on a real shower?
What other applications can it be used for?

## Slide 41: Real Showers
Shower started at time zero and continued for over ten minutes
Small Bracelet
Notes: It took me a day to understand what was going on here.
The temperature of the shower in a large apartment building is less a function of the setting of the handle, and more of a group consensus problem. This occurred to me the next day while standing in the shower. As it suddenly became scaldingly hot.

## Slide 42: Real Showers
Small Bracelet

## Slide 43: Real Showers
Small Bracelet
Notes: It took me a day to understand what was going on here.
The temperature of the shower in a large apartment building is less a function of the setting of the handle, and more of a group consensus problem. This occurred to me the next day while standing in the shower. As it suddenly became scaldingly hot.

## Slide 44: Real Showers
Small Bracelet

## Slide 45: Evaluation Criteria
How does it work at various water temperatures?
How well can it estimate start and stop times?
How well does it work on a real shower?
What other applications can it be used for?

## Slide 46: Extending the Idea
Thermes can be used anywhere a temperature differential exists

## Slide 47: Future Work
Better heat rejection
  Improved mechanical design is necessary
Cost of device
  Small form factor Peltier Junctions are expensive
Long-term deployment
  What kind of data can we gain from continuous data collection?

## Slide 48: Conclusion
Thermes
Energy-neutral thermal sensing
Reductionist Sensing
A new tool for ubiquitous and continuous sensing

## Slide 49: Questions?
Brad Campbell | bradjc@umich.edu
Branden Ghena | brghena@umich.edu
Prabal Dutta | prabal@eecs.umich.edu
Energy-Harvesting Thermoelectric Sensing for Unobtrusive Water and Appliance Metering
http://github.com/lab11/monjolo
Notes: Thank you very much

## Slide 50: Bonus Slides

## Slide 51: Wired Water Meters

## Slide 52: View of a Single Activation

## Slide 53: Energy Harvester Performance
Activations/min are proportional to temperature

## Slide 54: Energy Management is a Residential Problem
Energy use in the home is an important factor of total energy use
Water use is a significant portion of this problem.
US Energy Information Administration. 2012

## Slide 55: Water Is Becoming Scarce
“Water scarcity is among the main problems to be faced by many societies and the World in the XXIst century.” - Human Development Report 2006, UN

## Slide 56: Current Systems Fail to Maximize Usability
DoubleDip senses flow with an accelerometer
  Increases energy needs
DoubleDip board is 58 cm2 (9 in2)
  More obtrusive installation
These problems limit usability
DoubleDip

## Slide 57: DOE’s call for “open architecture sensors”
Source(s):
“Building Energy Efficiency Frontiers and Incubator Technologies (BENEFIT),” DE-FOA-0001027, 2014
“BTO [Building Technologies Office] is developing open-architecture sensors and sensor systems that easily share data to enable building operators and owners to cost effectively capture energy and cost savings through the use of new and existing control system applications. The objective is to take to market new sensors and sensor configurations that allow easy application to building operation, easy and open access to the data from the sensors, and novel application of sensor data to building management systems. BTO is particularly interested in innovative approaches that reduce the cost and power consumption for data collection of common building operation variables (temperature, pressure, relative humidity, etc.), open-source sensor packages that allow for data acquisition and transmission with increased lifespan between manual calibrations, “virtual sensors” enabled by innovative combinations of hardware and software, and easily installed “plug and play” sensor packages in which sensors would be automatically recognized by building energy management systems, in a manner similar to how conventional printers are easily recognized by an existing computer network.”
Notes: “BTO is developing open‐architecture sensors and sensor systems that easily share data to enable building operators and owners to cost effectively capture energy and cost savings through the use of new and existing control system applications. The objective is to take to market new sensors and sensor configurations that allow easy application to building operation, easy and open access to the data from the sensors, and novel application of sensor data to building management systems. BTO is particularly interested in innovative approaches that reduce the cost and power consumption for data collection of common building operation variables (temperature, pressure, relative humidity, etc.), open‐source sensor packages that allow for data acquisition and transmission with increased lifespan between manual calibrations, "virtual sensors" enabled by innovative combinations of hardware and software, and easily installed "plug and play" sensor packages in which sensors would be automatically recognized by building energy management systems, in a manner similar to how conventional printers are easily recognized by an existing computer network.”

## Slide 58: Measuring energy consuming activities
Monjolo: A Portuguese
water hammer

## Slide 59: Monjolo meter realizations
Test board
Plug-load
Panel-mount
Light-level